## Slide 1: Photoplethysmogram Acquisition
Yuning Wang

## Slide 2: Outline
Photoplethysmogram (PPG)
Advantages of PPG
PPG acquisition methods
Wearable devices
  Samsung smartwatches
Sensors with embedded systems
  SparkFun MAX30105 Particle and Pulse Ox Sensor with Arduino

## Slide 3: Photoplethysmogram (PPG)
Emitter or light source
Detector or light sensor
Red
Infrared
Green
Elsamnah, Fahed , et al. “Reflectance based organic pulse meter sensor for wireless monitoring of photoplethysmogram signal." Biosensors 9.3 (2019): 87.

## Slide 4: Advantages of PPG
Non-invasive
Acquiring heart rate， heart rate variability and SpO2
Easy to implement
Low-cost
Used in many clinical and commercial wearables
Can be used in remote health monitoring systems

## Slide 5: PPG acquisition methods
Wearable devices
  Fitbit, Samsung watch, Garmin, etc.
Sensors with Embedded system
https://iotdesignpro.com/projects/iot-heartbeat-monitoring-system-using-raspberry-pi

## Slide 6: Wearables
https://www.samsung.com/fi/wearables

## Slide 7: Samsung smartwatches
Provide raw PPG data with frequency = 20 Hz
Tizen OS
  Open source OS
  Customized application
    Web application HTML5 and javascript
    Native application C/C++
Internal memory
CPU
Limited battery life

## Slide 8: Considerations
Is the PPG frequency sufficient for your application?
  20 Hz can extract HR and some stress-related heart rate variability parameters reliably
Do you need to send the data to the cloud?
  Bluetooth, WiFi
How long do you want to collect data?
  Continuously
  5 minutes per hour

## Slide 9: Battery life
In case of continuous data collection battery last for less than 20 hours
Choose proper data collection duration
  Heart rate analysis: 30- 60 seconds is enough for
  Heart rate variability analysis
    Ultra short term analysis: less than 5 minutes
    Short term analysis: 5 minutes
    Long term analysis: 24 hours
Decide on intervals based on required battery life ( once per hours/per 4 hours/per day …)

## Slide 10: Sensors with Embedded system
SparkFun MAX30105 Particle and Pulse Ox Sensor
  Red, IR and green LEDs
  A photon detector
Microcontroller development board
  Arduino
Video link
https://learn.sparkfun.com/tutorials/max30105-particle-and-pulse-ox-sensor-hookup-guide

## Slide 11: Questions?